1)

Cases
Optimal case above is 2

Unless otherwise specified, all descriptions below have default settings when opening Design Analyzer. Design Analyzer was restarted for each case. Design Optimization was run multiple times with mapping effort changed – starting with the lowest setting and incrementally increased to indicated mapping effort for each case below.

All Low cases above were performed with low mapping effort

1) Medium mapping effort
Structure logic on (timing driven structuring on, boolean Optimization on)

2) (OPTIMIAL CASE)
High mapping effort
Structure logic off

3) High mapping effort
Structure logic off
Boundary Optimization on

4) High mapping effort
Structure logic on (timing driven structuring off, boolean Optimization on)

5) Medium mapping effort
Structure logic off
Flatten Logic on (high effort, multiple output, apply strategy)

6) High mapping effort
Structure logic on (timing driven structuring on, Boolean optimization on)
Flatten Logic on (high effort, multiple output, apply strategy)
Boundary Optimization on

2)

 ****************************************
Report : area
Design : FA
Version: X-2005.09
Date : Mon Mar 16 13:28:36 2015
****************************************

Library(s) Used:

    ece451_cells (File: /cad2/ece451/synopsys/ece451_cells.db)

Number of ports: 6
Number of nets: 20
Number of cells: 13
Number of references: 7

Combinational area: 617.399902
Noncombinational area: 1393.559937
Net Interconnect area: 0.284977

Total cell area: 2010.959961
Total area: 2011.244873
1
design_analyzer>
****************************************
Report : timing
        -path full
        -delay max
        -max_paths 1
Design : FA
Version: X-2005.09
Date : Mon Mar 16 13:28:36 2015
****************************************

Operating Conditions: nom_pvt Library: ece451_cells
Wire Load Model Mode: top

  Startpoint: a_reg (rising edge-triggered flip-flop clocked by clk)
  Endpoint: sum_out_reg
        (rising edge-triggered flip-flop clocked by clk)
  Path Group: clk
  Path Type: max

  Des/Clust/Port Wire Load Model Library
  ------------------------------------------------
  FA q35_27k ece451_cells

  Point Incr Path
  -----------------------------------------------------------
  clock clk (rise edge) 0.00 0.00
  clock network delay (ideal) 0.00 0.00
  a_reg/C (fdp2) 0.00 0.00 r
  a_reg/Q (fdp2) 0.57 0.57 f
  U38/Q (xo2p2) 0.40 0.97 r
  U34/NQ (xn2p2) 0.31 1.28 r
  sum_out_reg/D (fdp1) 0.00 1.28 r
  data arrival time 1.28

  clock clk (rise edge) 1.38 1.38
  clock network delay (ideal) 0.00 1.38
  sum_out_reg/C (fdp1) 0.00 1.38 r
  library setup time -0.09 1.29
  data required time 1.29
  -----------------------------------------------------------
  data required time 1.29
  data arrival time -1.28
  -----------------------------------------------------------
  slack (MET) 0.01