1) ALU Programming Table
Function	NotG	NotP	NotF	L	M	N
R + S	not(R ∧ S)	not(R ⊕ S)	not(R ⊕ S)	7	9	9
S - R	notR ∨ S	R ⊕ S	R ⊕ S	B	6	6
R - S	R ∨ notS	R ⊕ S	R ⊕ S	D	6	6
R ∨ S	1	R ∨ S	S	F	E	A
R ∧ S	1	R ∧ S	S	F	8	A
notR ∧ S	1	notR ∧ S	S	F	2	A
R ⊕ S	1	R ⊕ S	S	F	6	A
not(R ⊕ S)	1	not(R ⊕ S)	S	F	9	A

2) See next sheets.

3. a) Why shift guard is only necessary for the LSB? How can you modify the shifter structure such
that shift guard will be only necessary for the MSB to disconnect SL and FiPlus1 when shifting
does not occur?

The shifter sends Fi through the bottom two nfets by default, which are connected to notshl and notshr. The signal sent through the bottom half is connected to Fi_1, meaning driving a value for Fi_1 will change the value that RAMIN sees at the output. You could change this by substituting nmos for pmos, and vice versa, which would send the signal throug the top half of the structure. This also means that, when notshl and notshr are high, the signal is connected to FiPlus1, meaning you'd need a shifter guard for the MSB.

3. b) Which signals in Table 3 correspond to Bout and D signals given in Table 2?

D corresponds to notF, which are the final output of both.
Bout is represented by S – Bin – R, which just represents Cout because of the adder. It can be implemented as notG